Ichise’s Mutilinear Reference Tissue Model (MRTM)

Model Configurations and Assumptions

Assumptions: initial equilibration time t* for which the multi-linear relation hold

If the kinetics can be described by a 1-tissue compartment model, all data can be used for the fitting, i.e. t*=0. In this case b = (-1/k2) (c.f. eq. below)

There is a reference TAC C’(t) from a region without receptors, i.e. k3 = 0 (in the 2-tissue compartment model). The TAC C(t) from a receptor-rich region has k3>0

Operational Model Equation (MRTM0)

Application of the Logan plot for both TACs

{ int_0^{T} C(t)dt } over { C(T) } = { V } over { V' } { int_0^{T} C'(t)dt } over { C(T) } + { V } over { V'k_2' } { C'(T) } over { C(T) } + b

V and V’ are the total distribution volumes of C(t) and C’(t) resp. while k’2 is the clearance rate constant from the reference region to the plasma, b is the intercept term which becomes constant for T>t*

Allowing for three fit parameters: A= V/V’, B = V/(V’k’2), C = b

From this parameters we can calculate the binding potential to be: BP = V/V’ - 1.0 assuming that the non-displaceable distribution volumes in the tissue and reference regions are identical

This equation is applicable to both 1T and 2T compartment models

Problem: Assumption of noise-free variables

1T model: V = K1/k2, V’=K1’/k2’, R1 = K1/K1’ → R1 = -(V/V’k2)/b

Noise-Treatment (MRTM)

Correlation of noisy terms on the r.h.s. and l.h.s. produce biased estimates

Following multi-linear reference tissue model:

C(T) = - { V } over { V'b } int_0^T C'( t )dt + { 1 } over { b } int_0^T C( t ) dt - { V } over { V'k_2' b } C'( T )

Now, only the integral of C(t) is present on the r.h.s. such that the noisy part is reduced significantly

Fit-parameters: A = -V/(V’b) , B = 1/b, C = -V/(V’k2’,b)

Calculation of BP = -(A/B + 1)

1T model: R1 = C and k2 = -B

Estimation of k2’ via k2’ = A/C

→ although there is only one true value of k2’, taking a fixed average k2’ value from the MRTM analysis can yield input for the MRTM2 model

MRTM2

Taking a fixed k2’ into account, one can derive an equation with only two parameters to fit:

C(T) = - { V } over { V'b } ( int_0^T C'( t )dt + { 1 } over { k_2' } C'( T )) + { 1 } over { b } int_0^T C( t ) dt

Which leads to the fit coefficients A = -(V/V’b) and B = 1/b and the binding potential
BP = -(A/B + 1)